Wide-Area Networks and Metropolitan Area Networks
Wide-Area Networks
and
Metropolitan Area Networks
Gihan Dias
CS303
060722

---
What is a WAN?
What is a WAN?
- A network which spans a wide area
- Typically over 30 km in diameter
- Distinguished from a LAN
  - which is generally < 1km diameter
- WANs are operated by telecom service providers
- LANs are run by individual orgs
Distance limits depend on the situation where we are going to build the network

---
What is a MAN?
What is a MAN?
A network which spans a metropolitan area
  - E.g. Colombo Metro – Moratuwa to Ja-Ela
- Up to 50 km or so in diameter
- Run by Telecom providers

---
LANs, MANs and WANs
LANs, MANs and WANs
- Traditionally, different technologies were used for LANs MANs and WANs
- Now they are converging
  - Ethernet is used in all three types of networks
1. Leased Lines => if it is 200Mbps, they will give exactly that amount to the customer, expensive
2. Broadband => if it is 200Mbps, we will get less than that, cheap

---
Contents of this presentation
Contents of this presentation
Technologies which are primarily used in WANs and MANs

---
Topics
Topics
- Leased Lines
- Packet switching
- X.25
- Frame Relay
- ATM
- MPLS
- Metro Ethernet

---
Telecom Networks
Telecom Networks
Access
Transmission
Switches
Subcribers

---
Leased Line
Leased Line
A full-time dedicated link from one point to another
  - is always available for you, 24 hours
- Specified carying capacity (e.g., 64kb/s, 2Mb/s, 155Mb/s)
- Fixed monthly cost
  - Irrespective of usage

---
Types of Leased Lines
Types of Leased Lines
- Analog
- Digital
  - today, most leased lines are digital
Speed:
  - 64kb/s - 2Mb/s is most common
  - 64kb - for a few computers
  - 2MB - for a large office

---
Uses of Leased Lines
Uses of Leased Lines
Voice
  - tie lines
Data
  - corporate networks
  - Internet access
- Voice+Data
- Data Networks used to be implemented using leased lines

---
Packet Switching
Packet Switching
- Breaks a stream of data in to a set of units called packets
- Packets are sent one-after-another to the network
- The network forwards each packet from source to destination
- Packets from different connections are interspersed in the network
- More efficient than leased lines for bursty traffic

---
Types of Packet Switching
Types of Packet Switching
Datagram
  - Each packet is routed independently
Virtual circuit
  - Routing is done once for each connection (or flow)
  - Uses connection identifiers
  - Still no dedicated circuit

---
X.25 Packet Switching
X.25 Packet Switching
- X.25 is the ITU standard for the user interface to a packet data network
- Introduced in the 1960s
- Became the standard for data communication
- Used by banks, airlines, etc.
- Very expensive (when compared with today’s networks)
- Very slow (~64kb/s)

---
Frame Relay
Frame Relay
- Wide-area network technology
- Replacement for X.25
- Virtual-circuit oriented
- Relays frames from one point to another
- Can be used to carry IP datagrams
  - can thus be viewed as link layer by IP
A datagram is a self-contained, independent unit of data that carries sufficient information to be routed from the source to the destination without relying on earlier exchanges.

---
Frame Relay
the methods used to prevent network overload and ensure smooth data flow
- Designed in late ‘80s, widely deployed in the ‘90s
- Frame relay service:
  - no error control – assumes NW is reliable
  - end-to-end congestion control

---
Frame Relay (cont.)
Frame Relay (cont.)
Designed to interconnect corporate LANs
  - typically permanent VC’s: “pipe” carrying aggregate traffic between two routers
- Multiple VCs in one physical link
- Corporate customer leases FR service from public Frame Relay network
- Committed Information Rate (CIR)
  - defined data rate, “guaranteed” for each VC
  - negotiated at VC set up time
  - customer pays based on CIR

---
Asynchronous Transfer Mode (ATM)
Asynchronous Transfer Mode (ATM)
Data is transmitted and switched in small units called cells (53 bytes)
  - Cell Switching
Suitable for data as well as voice and video
Header - 5 bytes
Data - 48 bytes
An ATM Cell

---
Why Cell Switching?
Why Cell Switching?
- Need transmission of voice, video, and data
- These can no longer be separated
- In X.25 and Frame Relay the switching delay is unacceptable for voice and video
- Therefore, a switching topology that integrates voice, video and data is needed
- Cells can be processed very fast
  - Uniform size, simple header

---
ATM
ATM
- Small cells enables the same technology to be used for any kind of service
- Scalable and flexible
- Flexible charging schemes based on the number of cells transmitted is possible
  - Bandwidth is not fixed at 64 kb/s 2 Mb/s etc.
Generally uses optical fiber as the transmission medium

---
ATM:  network or link layer?
ATM: network or link layer?
Vision: end-to-end transport: “ATM from desktop to desktop”
  - ATM is a network technology
Reality: used to connect IP backbone routers
  - ATM as switched link layer, connecting IP routers
Vision → Network
Reality → Link

---
ATM Layer: Virtual Circuits
ATM Layer: Virtual Circuits
- VC transport: cells carried on VC from source to dest
- each packet carries VC identifier
  - not destination ID
- every switch on source-dest path maintains “state” for each passing connection
- resources (b/w, buffers) may be allocated to VC to get circuit-like performance

---
ATM
Virtual Path Identifier
GFC
VPI
VPI
VCI
Virtual Circuit Identifier
VCI
The two-part addressing makes network routing easier and faster
VCI
PT
HEC
VCI 1
VCI 1
VCI 2
VCI 2
VPI
VCI 3
VCI 3

---
A Comparison
A Comparison
Outdated → Need to be update these data
Frame Relay
X.25
ATM
Connection Oriented
Yes
Yes
Yes
Normal speed (Mb/s)
0.64
2
155
Switched
Yes
No
Yes
Max. payload (bytes)
128
1600
48
Permanent VCs
Yes
Yes
Yes
Multicasting
No
No
Yes

---
MPLS
MPLS
- MPLS – Multi-protocol Label Switch: Multi-protocol because can be applied for any layer 2 network protocol
- MPLS is a natural evolution of Internet. It is based on IP and routing protocols such as BGP-4,OSPF and IS-IS
- Typically MPLS only resides in service providers or carrier network and not in private networks

---
MPLS Protocol Stack
MPLS Protocol Stack
Application
IP or Multi-Service
MPLS
Layer 2 (PPP, ATM, FR,..)
Physical

---
MPLS enables Convergence
MPLS enables Convergence

---
What is MPLS ?
What is MPLS ?
- MPLS provides connection oriented switching based on a label applied at the edge of an MPLS domain.
- IP is used to signal MPLS connections.
- Major Applications are:
  - Network Scalability
  - Traffic Engineering
  - VPNs

---
Key MPLS Capabilities
Key MPLS Capabilities
Network Scalability
Traffic Engineering
VPN’s
IP Multicast
IP CoS
RSVP

---
MPLS - Best Of Both Worlds
MPLS - Best Of Both Worlds
PACKET
Forwarding
Packet
SWITCHING
HYBRID
ATM/FR
Performance
Connection Oriented
Traffic Engineering
Security
QoS
Scalable
Flexible
Easily Deployable
Inexpensive
Dynamic Routing
Route at the Edge & Switch at the Core
MPLS
IP

---
Ethernet First Mile (EFM)
Ethernet First Mile (EFM)
- connect homes and offices using Ethernet
- IEEE 802.3ah standard
- Media
  - Copper
  - Fibre
Data, Physical layers can use any tech, but others should have MPLS overlays
MPLS are going in the same link as the other data, so to seperate them we use MPLS headers

---
Ethernet First Mile over Copper (EFMC)
Ethernet First Mile over Copper (EFMC)
- uses DSL modulation schemes with Ethernet frames
- objectives
  - 10 Mbps at 750m (EFMC SR) and
  - 2 Mbps at 2,700m (EFMC LR)
  - existing products deliver higher throughput to longer distances

---
Ethernet First Mile over Fibre (EFMF)
Ethernet First Mile over Fibre (EFMF)
- Point-to-Point
- Passive Optical Networks (PON)
- Dual fiber standards
  - 100BASE-LX10
  - 1000BASE-LX10
Single fiber standards
  - 100BASE-BX10
  - 1000BASE-BX10

---
Summary
Summary
- Many types of Wide-Area Networks
- MPLS and Ethernet are becoming the most prevalent
- Technology will keep changing