Wide-Area Networks and Metropolitan Area Networks
Wide-Area Networks
and
Metropolitan Area Networks
Gihan Dias
CS303
060722

---
What is a WAN?
What is a WAN?
- A network which spans a wide area
- Typically over 30 km in diameter
- Distinguished from a LAN
  - which is generally < 1km diameter
- WANs are operated by telecom service providers
- LANs are run by individual orgs

---
What is a MAN?
What is a MAN?
A network which spans a metropolitan area
  - E.g. Colombo Metro – Moratuwa to Ja-Ela
- Up to 50 km or so in diameter
- Run by Telecom providers

---
LANs, MANs and WANs
LANs, MANs and WANs
- Traditionally, different technologies were used for LANs MANs and WANs
- Now they are converging
  - Ethernet is used in all three types of networks

---
Contents of this presentation
Contents of this presentation
Technologies which are primarily used in WANs and MANs

---
Topics
Topics
- Leased Lines
- Packet switching
- X.25
- Frame Relay
- ATM
- MPLS
- Metro Ethernet

---
Telecom Networks
Telecom Networks
Access
Transmission
Switches
Subcribers

---
Leased Line
Leased Line
A full-time dedicated link from one point to another
  - is always available for you, 24 hours
- Specified carying capacity (e.g., 64kb/s, 2Mb/s, 155Mb/s)
- Fixed monthly cost
  - Irrespective of usage

---
Types of Leased Lines
Types of Leased Lines
- Analog
- Digital
  - today, most leased lines are digital
Speed:
  - 64kb/s - 2Mb/s is most common
  - 64kb - for a few computers
  - 2MB - for a large office

---
Uses of Leased Lines
Uses of Leased Lines
Voice
  - tie lines
Data
  - corporate networks
  - Internet access
- Voice+Data
- Data Networks used to be implemented using leased lines

---
Packet Switching
Packet Switching
- Breaks a stream of data in to a set of units called packets
- Packets are sent one-after-another to the network
- The network forwards each packet from source to destination
- Packets from different connections are interspersed in the network
- More efficient than leased lines for bursty traffic

---
Types of Packet Switching
Types of Packet Switching
Datagram
  - Each packet is routed independently
Virtual circuit
  - Routing is done once for each connection (or flow)
  - Uses connection identifiers
  - Still no dedicated circuit

---
X.25 Packet Switching
X.25 Packet Switching
- X.25 is the ITU standard for the user interface to a packet data network
- Introduced in the 1960s
- Became the standard for data communication
- Used by banks, airlines, etc.
- Very expensive (when compared with today’s networks)
- Very slow (~64kb/s)

---
Frame Relay
Frame Relay
- Wide-area network technology
- Replacement for X.25
- Virtual-circuit oriented
- Relays frames from one point to another
- Can be used to carry IP datagrams
  - can thus be viewed as link layer by IP

---
Frame Relay
- Designed in late ‘80s, widely deployed in the ‘90s
- Frame relay service:
  - no error control – assumes NW is reliable
  - end-to-end congestion control

---
Frame Relay (cont.)
Frame Relay (cont.)
Designed to interconnect corporate LANs
  - typically permanent VC’s: “pipe” carrying aggregate traffic between two routers
- Multiple VCs in one physical link
- Corporate customer leases FR service from public Frame Relay network
- Committed Information Rate (CIR)
  - defined data rate, “guaranteed” for each VC
  - negotiated at VC set up time
  - customer pays based on CIR

---
Asynchronous Transfer Mode (ATM)
Asynchronous Transfer Mode (ATM)
Data is transmitted and switched in small units called cells (53 bytes)
  - Cell Switching
Suitable for data as well as voice and video
Header - 5 bytes
Data - 48 bytes
An ATM Cell

---
Why Cell Switching?
Why Cell Switching?
- Need transmission of voice, video, and data
- These can no longer be separated
- In X.25 and Frame Relay the switching delay is unacceptable for voice and video
- Therefore, a switching topology that integrates voice, video and data is needed
- Cells can be processed very fast
  - Uniform size, simple header

---
ATM
ATM
- Small cells enables the same technology to be used for any kind of service
- Scalable and flexible
- Flexible charging schemes based on the number of cells transmitted is possible
  - Bandwidth is not fixed at 64 kb/s 2 Mb/s etc.
Generally uses optical fiber as the transmission medium

---
ATM:  network or link layer?
ATM: network or link layer?
Vision: end-to-end transport: “ATM from desktop to desktop”
  - ATM is a network technology
Reality: used to connect IP backbone routers
  - ATM as switched link layer, connecting IP routers

---
ATM Layer: Virtual Circuits
ATM Layer: Virtual Circuits
- VC transport: cells carried on VC from source to dest
- each packet carries VC identifier
  - not destination ID
- every switch on source-dest path maintains “state” for each passing connection
- resources (b/w, buffers) may be allocated to VC to get circuit-like performance

---
ATM
Virtual Path Identifier
GFC
VPI
VPI
VCI
Virtual Circuit Identifier
VCI
The two-part addressing makes network routing easier and faster
VCI
PT
HEC
VCI 1
VCI 1
VCI 2
VCI 2
VPI
VCI 3
VCI 3

---
A Comparison
A Comparison
Frame Relay
X.25
ATM
Connection Oriented
Yes
Yes
Yes
Normal speed (Mb/s)
0.64
2
155
Switched
Yes
No
Yes
Max. payload (bytes)
128
1600
48
Permanent VCs
Yes
Yes
Yes
Multicasting
No
No
Yes

---
MPLS
MPLS
- MPLS – Multi-protocol Label Switch: Multi-protocol because can be applied for any layer 2 network protocol
- MPLS is a natural evolution of Internet. It is based on IP and routing protocols such as BGP-4,OSPF and IS-IS
- Typically MPLS only resides in service providers or carrier network and not in private networks

---
MPLS Protocol Stack
MPLS Protocol Stack
Application
IP or Multi-Service
MPLS
Layer 2 (PPP, ATM, FR,..)
Physical

---
MPLS enables Convergence
MPLS enables Convergence

---
What is MPLS ?
What is MPLS ?
- MPLS provides connection oriented switching based on a label applied at the edge of an MPLS domain.
- IP is used to signal MPLS connections.
- Major Applications are:
  - Network Scalability
  - Traffic Engineering
  - VPNs

---
Key MPLS Capabilities
Key MPLS Capabilities
Network Scalability
Traffic Engineering
VPN’s
IP Multicast
IP CoS
RSVP

---
MPLS - Best Of Both Worlds
MPLS - Best Of Both Worlds
PACKET
Forwarding
Packet
SWITCHING
HYBRID
ATM/FR
Performance
Connection Oriented
Traffic Engineering
Security
QoS
Scalable
Flexible
Easily Deployable
Inexpensive
Dynamic Routing
Route at the Edge & Switch at the Core
MPLS
IP

---
Ethernet First Mile (EFM)
Ethernet First Mile (EFM)
- connect homes and offices using Ethernet
- IEEE 802.3ah standard
- Media
  - Copper
  - Fibre

---
Ethernet First Mile over Copper (EFMC)
Ethernet First Mile over Copper (EFMC)
- uses DSL modulation schemes with Ethernet frames
- objectives
  - 10 Mbps at 750m (EFMC SR) and
  - 2 Mbps at 2,700m (EFMC LR)
  - existing products deliver higher throughput to longer distances

---
Ethernet First Mile over Fibre (EFMF)
Ethernet First Mile over Fibre (EFMF)
- Point-to-Point
- Passive Optical Networks (PON)
- Dual fiber standards
  - 100BASE-LX10
  - 1000BASE-LX10
Single fiber standards
  - 100BASE-BX10
  - 1000BASE-BX10

---
Summary
Summary
- Many types of Wide-Area Networks
- MPLS and Ethernet are becoming the most prevalent
- Technology will keep changing