The Data Link Layer
The Data Link Layer
Gihan Dias
CS303- May 2007

---
Data Link Layer
Data Link Layer
Application
7
Presentation
6
Session
5
Transport
4
Network
3
Data Link
2
Physical
1

---
Functions of the DLL
Functions of the DLL
- Synchronisation
- Error control
- Flow control
- Data compression
- Encryption

---
Additionally – for Shared Media
Additionally –
for Shared Media
Media access control
  - control the access of the shared medium by each station
Logical link control
  - functions in the previous slide
Why MAC?
- Using the MAC address we can separately identify stations while using Shared Medium without conflicts

---
Synchronisation
Synchronisation
Objective:
  - To identify the beginning and end of data
- At the data-link layer, data are divided into units
- The receiver must be able to distinguish the beginning and end of each unit
We use delimiters to show the boundary between 2 frames

---
Types of synchronisation
Types of synchronisation
Fixed-length (No need of delimiters)
  - byte (e.g., asynchronous transmission)
  - Cell
Variable length
  - data is divided in to frames

---
Frame
Frame
A link-layer data unit is called a frame, and encapsulates a packet
Frame
header
Frame
trailer
frame (data-link)
data
message (app)
segment (transport)
packet (network)

---
Frame delimitation
Frame delimitation
- Character count
- Character-oriented
  - beginning and end of frames are identified by STX and ETX characters
Bit-oriented
  - frames are delimited by flag sequence

---
Character-oriented Framing
Character-oriented Framing
ESC = “\”
Just like in programming languages
(a) A frame delimited by flag bytes.
(b) Four examples of byte sequences before and after stuffing.

---
Bit-oriented Framing
Bit-oriented Framing
Data frame 1:
011100010101111000110
Data frame 1 with flag sequences:
0111111001110001010111100011001111110
Data frame 2:
011100010111111000110
Data frame 2 with stuffed bit:
0111000101111101000110
Data frame 2 with flags:
01111110011100010111110100011001111110

---
Problems with Synchronisation
Problems with Synchronisation
- Data loss (e.g. ETX or flag)
- Data errors
- Control char or flag may appear in data

---
Error Control
Error Control
Physical transmission may introduce errors
  - missing bits
  - inserted bits
  - changed bits – 10, 0 1
Errors often occur in bursts
Sudden breaks
error
error
error burst

---
Error Control
We need to
  - detect errors
  - correct errors or deal with errored data appropriately
  - Even we can’t correct, we have to at least detect them

---
Error Detection
Error Detection
Introduce additional data into frame
  - Parity
  - Checksum
  - Cyclic redundancy check (CRC)
- all methods can detect only some errors
- residual errors will exist
- prob. of residual errors should be low
- how to deal with residual errors?

---
Error Detection
EDC= Error Detection and Correction bits (redundancy)
D = Data protected by error checking, may include header fields

---
Error-Detecting Codes
Error-Detecting Codes
Calculation of the
polynomial code checksum.

---
Error Correction
Error Correction
- Forward Error Correction
- Automatic Repeat Request (ARQ)

---
Forward Error Correction
Forward Error Correction
- Redundancy is added to data stream
- Sufficient to recover original data even if some errors occur
  - simplex transmission
  - CD-ROMs
  - high-latency links
Residual error rate may be high

---
Forward Error Correction (cont..)
Forward Error Correction (cont..)
May be used where low latency is more important than low error rate
  - e.g. voice, video
the sender sends a redundant error-correcting code along with the data frame. The receiver performs necessary checks based upon the additional redundant bits. If it finds that the data is free from errors, it executes error-correcting code that generates the actual frame. It then removes the redundant bits before passing the message to the upper layer

---
Automatic Repeat Request - ARQ
Automatic Repeat Request -
ARQ
Idle RQ (stop and wait)
  - link utilisation may be low
Continuous RQ
  - sliding window protocols
Extra – Piggy Bank
Sending some set of data from the previous and the next data sets. So if the previous data are with errors or next, they can be recovered using those extra data.

---
Idle RQ (stop and wait)
Idle RQ (stop and wait)
sender
time-out
wait
data
re-sent
data
lost
data
data
ack
ack
x
receiver
2 ways of not going ack

---
Continuous ARQ
Continuous ARQ
a counter (state variable) is maintained at both ends
  - V(S) - send state variable - sequence number of next frame to be sent
  - V(R) - receive state variable - sequence number of expected frame
- frames are sent with V(S)
- ACK is sent with V(R), if frame does not have errors and then sender can free the corresponding frame from the window

---
Continuous ARQ
if a frame is erroneous, a NAK is sent
  - NAK is called Reject or Selective Reject
for V(S) and V(R), a 3-bit field is often used
  - 8 numbers (000 to 111) - window size is 7
if n bits are send and no ACK comes the sender waits till an ACK comes
No problem in getting more than one same packet until it satisfied with the ack. Duplicates will be discarded after the ack is done

---
Continuous ARQ (Go Back N)
Continuous ARQ (Go Back N)
Keep these data safely. Receiver is capable in collecting many pending data
(a) Receiver’s window size is 1.
(b) Receiver’s window size is large.

---
Flow control
Flow control
In-band
  - X-ON / X-OFF
Out-of-Band
  - CTS / RTS
In conjunction with error control
  - by manipulation the size of the sliding window

---
Data compression
Data compression
- Based on probability theory
- Prob of each symbol is unequal
  - P(“e”) >> P(“x”)
Prob of next symbol is based on previous ones
  - Electroni?

---
Encryption
Encryption
Used to Ensure
  - Privacy (confidentiality)
  - Authenticity
Based on an encryption algorithm and a key
  - single-key encryption
  - public-key (two-key) encryption

---
Medium Access Control
Medium Access Control
Primary / Secondary
Peer-to-peer

---
Primary / Secondary
Primary / Secondary
Polling
  - stop and wait
  - continuous ARQ
non-Polling
  - RTS/CTS
  - Time-Division Multiple Access (TDMA)
When a node wants to transmit data to another node, it sends out a RTS 'Request to Send' packet. The receiver node replies with a packet called CTS 'Cleared to Send' packet.After the transmitter node receives the CTS packet, it transmits the data packets.

---
Poll/Select Systems
Poll/Select Systems
Poll
  - Do you have data for me?
Select
  - I have data for you and I am selecting you. Can you receive?

---
Non-polling Systems
Non-polling Systems
- RTS/CTS
- Widely used since RS-232-C uses the same method
RTS
CTS
Data
CTS Off
Data

---
TDMA (Time Division Multiple Access)
TDMA
(Time Division Multiple Access)
- used in satellite networks
- one site is designated as master (reference) station
- when secondary stations wish to use the channel, they indicate that to reference station
- reference station periodically transmits control information indicating which station can use the channel during each time-slot

---
Peer-to-peer
Peer-to-peer
- Time Division Multiplexing (TDM)
- Aloha
- Carrier Sense Multiple Access - CSMA
- Token Ring
- Token Bus

---
TDM
TDM
- Time-Division Multiplexing
- simplest of peer to peer
- each station is given a pre-assigned time-slot
- transmits only in that time-slot
- found in both LANs and WANs

---
ALOHA
ALOHA
A station transmits whenever it has data to send
  - there will sometimes be collisions between packets sent by two or more stations
- Stations detect the collision and re-transmit
- performance degrades when traffic is high

---
Pure ALOHA
Pure ALOHA
In pure ALOHA, frames are transmitted at completely arbitrary times.

---
Carrier Sense Multiple Access CSMA
Carrier Sense Multiple Access
CSMA
Each station monitors the channel and transmits only when the channel is free
  - collisions may still occur if two stations transmit almost simultaneously

---
CSMA with collision detection CSMA-CD
CSMA with collision detection
CSMA-CD
- stations monitor channel while transmitting
- aborts transmission if it detects a collision
- waits a random period of time before re-transmitting
  - why a random time?
Otherwise both stations send data again at the same time

---
CSMA with Collision Detection
CSMA with Collision Detection
CSMA/CD can be in one of three states: contention, transmission, or idle.

---
Carrier Sense Systems (Collision Free)
Carrier Sense Systems
(Collision Free)
Similar to Carrier Sense (collision) networks
  - difference is logic is used to prevent collisions
Two approaches:
  - a timer or arbiter determines when a station can transmit without danger of collisions
  - each station has a pre-determined timing threshold
    - timing can be established on priority basis
  - Can use techniques similar to priority slot n.w.

---
Token Ring
Token Ring
- The network has a logical ring structure (may have a different physical structure)
- a token is passed around while the ring is idle
[Speaker Notes: there must be only one token in this scheme (although the "slotted" ring scheme described later can be seen as a multi-token scheme) (the scheme continues on next slide)]

---
Token Ring
any node wishing to transmit a message must:
  - wait until a Free token arrives:
  - remove it, and send a Busy token plus message:

---
Token Ring
- Tx station waits until the Busy token returns, then removes it and data
- transmits a Free token
[Speaker Notes: after these four stages, the ring is back where it was, except the next node gets first chance to transmit if the node that just transmitted want to send again immediately, it must wait until all others have had a chance]

---
Token Ring
- needs mechanisms to set up and maintain the token
- these mechanisms must be
  - either centralised (hence single-point-of-failure)
  - or distributed (more complex, more expensive)
[Speaker Notes: how does the token get there in the first place? and how does it get replaced if it gets lost? some rings have a special monitor node that restores the token if something goes wrong others share this duty among all stations (needs a clever scheme to avoid getting several replacement tokens!) note that the only "wasted" activity is the circulation of the token, and when the ring is busy, this is a small proportion of total activity. I.e. busy token ring networks work efficiently (unlike busy CSMA/CD networks)]

---
Token Ring
strengths:
  - fairer and more efficient than CSMA/CD when traffic is heavy
  - all nodes are guaranteed a chance to transmit within some fixed time
weaknesses:
  - complexity
  - delays awaiting the token
  - Single point of failure (token – if token is missing everybody will be waiting)

---
Token Bus
Token Bus
- combines ring topology with bus topography
- nodes form a virtual ring
- a token circulates from node to node in sequence,
  but is transmitted via the bus
[Speaker Notes: this is ingenious and sophisticated, and needs careful explanation transmission occurs by broadcasting on a bus but is arbitrated by passing a token around in a "virtual" ring, I.e. in an agreed sequence hence CSMA/CD is not required, because only one node will transmit at a time]